# Eufhemism
## Group members
Name	Student number
Darren Andrew	0528679
Mansour Kheffache	0528776
Sami Kabir	0528747
Vesa Ylämäki	0507933

## pysäköid.ai
### Vision
We envision an autonomous parking facility for vehicle, where all processes required for daily operations are fully automated without the need for human assistance, while having a low carbon footprint.
### Components
- Parking Slot Allocation
- Energy-Based Payment
- Adaptive HVAC + Lighting
- Automated Cleaning and Waste Disposal
- Automatic Fault Detection
## Technology
On the surface:
Drive-in
Allocate parking spot
Get directions
Plug car to micro-grid
Do “stuff”
Come back to car, and leave
Behind the Scenes:
Fleet management
HVAC + Lighting adapt to utilization
Draws energy from cars depending on time
Automatically decides areas to clean
Report a fault in case of malfunction
### Architecture

### Screen caps
## Protocol
#### UPB - Universal Powerline Bus
- for communication among devices
- uses powerline wiring for signaling and control
- developed by PCS (Powerline Control Systems, Northridge CA)
- released 1999
- based on concept of X10 standard
  - inproved transmission rate
  - higher reliability > 99 % (X10 70-80 %)
##### Physical communication method
Digitally encoded information is sent over the electrical powerline as a series of precisely timed pulses. The pulses are superimposed on top of the AC sine wave.

Fig. 1 UPB Pulse
Fig. 1 UPB Pulse
Pulses are generated by charging a capacitor in the transmitter and then discharging it. A pulse can be sent once on each half-cycle. One pulse transmits two bits of information. Pulse value is selected by timing the pulse on one of four predefined positions. Transmitter tolerance for timing is ±40 μs.

Fig. 2 UPB Timing
UPB works on single-phase, split-phase and 3-phase powerlines.
##### Data communications
The UPB Byte forms of four pulses (8 bits).

Fig. 3 The standard UPB Communication Packet
The first byte of the packet is called a preamble byte and it is used for synchronization on the receiver device. Preamble byte is always form of 2-1-1-2. The packet header contains information about the packet size, source, destination etc.

Fig. 4 The Packet Header
##### The UPB System model

Fig. 5 UPB system model

Fig. 6 Setup register

Fig. 7 Linking components
## If we had more time
Only having a few day to work on the project was not ideal and we only had a chance to implement a few ideas. There was a few more sensors and logic we would of liked to implement into the prototype if we had more time.
Table- with things we wanted to do.
## Poster
## Documents
Final report: Final presentation: Link to code: